## Slide 1: Pulse Width Modulation Using ( Graphical LCD and ATmega32 ) Amit Graduation Project
Introduced by: MOHAMED AHMED MOSTAFA KHALIL.
Group NASR83..

## Slide 2: OverView
-PWM drawer works as a mini oscilloscope that is responsible for printing the frequency and the waveform of the generated PWM signal.
-(PWM) is a modulation technique that generates variable-width pulses to represent the amplitude of an analog input signal. The output switching transistor is on more of the time for a high-amplitude signal and off more of the time for a low-amplitude signal.

## Slide 3: - period of a pulse consists of an ON cycle (5V) and an OFF cycle (0V). The fraction for which the signal is ON over a period is known as the duty cycle.
Frequency signals, or other waves, expresses the number of cycles of the repetitive waveform per second.
Duty Cycle (In %) = Ton /total period *100

## Slide 5: -Finally, we can use PWM in many applications, ranging from communications to power control and conversion -For example, the PWM is commonly used to control the speed of electric motors, the brightness of lights, ultrasonic cleaning applications, and many more.

## Slide 6: Layered Architicture
Application Layer
PWM DRAWER
G-LCD
Hardware Abstraction Layer
Micro-Controller Abstraction Layer
PWM
GPT
DIO
ICU

## Slide 7: Flow Chart

## Slide 12: Thank You